## Slide 1
2D Mesh Network-on-Chip (NoC)
SystemVerilog Architecture, Router Switching, and Simulation Analysis
Designed and Presented by Gowsh

## Slide 2
1. Introduction: Why NoC?
The Bus Limitation Problem
• Traditional shared buses (e.g. AMBA AHB) do not scale as IP cores count increase.
• Crossbar complexity grows quadratically O(N^2), causing routing and wiring bottlenecks.
NoC: The Scalable Grid Solution
• Replaces global buses with a structured local micro-network of switches/routers.
• Promotes concurrent transactions, leading to high aggregated network bandwidth.

## Slide 3
2. Topology: 2D Mesh Structure
• Grid Layout: Routers are organized in a 2D coordinate space (X, Y).
• Node Connections: Each router communicates with up to 4 neighbors (East, West, North, South) and 1 local Processing Element (PE).
• Bidirectional Links: Neighboring nodes are connected by dedicated pairs of forward and backward routing paths.
• Grid Address: Node coordinates represent its address. In this design, coordinates dest_x and dest_y are 2 bits each, mapping a 4x4 mesh (16 nodes, ID 0 to 15).

## Slide 4
3. Switch Microarchitecture: 5x5 Router
• Port Configurations: 5 inputs and 5 outputs matching LOCAL, EAST, WEST, NORTH, and SOUTH interfaces.
• Elastic Input Buffer: A 1-entry register slice per input port stores packets dynamically. This breaks long physical wires and resolves combinational paths.
• Zero-Bubble Handshake: Handshaking logic implements a lookahead accept-release path. Ready goes high if a buffer is empty OR currently releasing data, allowing back-to-back single-cycle packet streaming.
• Crossbar MUX: Connects inputs to winning outputs combinatorially based on arbitrated grant permissions.

## Slide 5
4. Routing Algorithm: XY Deterministic Routing
• Routing Steps: Packet travels in X-direction horizontally until it hits column address, then Y-direction vertically, then Local interface.
• Deadlock Prevention: Deadlocks happen when packets get stuck in a cyclic loop. XY routing mathematically guarantees zero cyclic loops because turn transitions from Y back to X are strictly forbidden.
• Wire-Based Decoding: The destination port is calculated on-the-fly (combinatorially) by comparing coordinates, requiring no routing tables or register maps.
• Packet format: [7:6] Dest X | [5:4] Dest Y | [3:0] Data Payload

## Slide 6
5. Flow Control & Arbitration
• Valid-Ready Protocol: Data transfer happens on rising clock edge if and only if both Valid (transmitter has data) and Ready (receiver is free) are high.
• Round-Robin Allocation: A dynamic round-robin arbiter manages collision control when multiple input ports compete for the same output port, rotating priority pointers to avoid starving nodes.
• Backpressure Propagation: When a receiver (PE) deasserts ready, the local router buffer fills up, deasserts its incoming ready ports, propagating stall states backward without loss of packet data.

## Slide 7
6. Verification & Results
Exhaustive Simulation Campaigns (All Tests Passed)
• 16x16 Directed Test: Checked all 240 combinations of source-destination node coordinates. 100% of packets routed successfully.
• Single Destination Congestion: Flooded Destination 15 from 15 sources simultaneously. Verified round-robin fairness and correct flow control.
• 20,000 Packet Random Stress Test: Ran continuous packet streams with randomized destinations and randomized receiver backpressures. All 20,000 packets were delivered with zero drops or deadlocks.

## Slide 8
Thank You!
Q & A